## Slide 1: USGS DIGITAL TERRAIN MODELS AND MOSAICS FOR LMMP
M. R. Rosiek, E. M. Lee, E. T. Howington-Kraus, R. L. Fergason, L. A. Weller, D. M. Galuszka, B. L. Redding, O. H. Thomas, R. A. Saleh, J. O. Richie, J. R. Shinaman, B. A. Archinal, and T. M. Hare
U.S. Geological Survey
2255 N. Gemini Dr.
Flagstaff, AZ, 86001
mrosiek@usgs.gov spell out dtms
Notes: I am not set on the colors so these may change

## Slide 2: LMMP background
Lunar Precursor Robotic Program
  Marshall Space Flight Center (LPRP/MSFC)
Tasked by the Advanced Capabilities Division
  Results of LRO easily accessible and usable by the Constellation Program (CxP)
  2007 – Lunar Mapping and Modeling Program (LMMP) start date
Goals for Lunar Mapping and Modeling Program (LMMP)
  Develop and integrate a suite of lunar mapping and modeling tools and products to support CxP and other lunar exploration activities
  Leverage products and expertise provided by the LRO Science Teams
  Identify and leverage other areas where NASA has made investments in relevant activities and expertise
    ARC, Arizona State University, CRREL (Army Cold Regions Research & Engineering Laboratory), GSFC, JPL, & USGS
Notes: Back in 2007 the Lunar Precursor Robotic Program , located at Marshall Space Flight Center, was tasked by the Advanced Capabilities Division with support to the Constellation Program. This Program became know as the Lunar Modeling and Mapping Program. One of the goals of the program was to develop and integrate Lunar mapping and modeling tools and products to support the Constellation Program and other Lunar Exploration activities. This was leveraged of existing Programs and activities. The expertise within the Lunar Reconnaissance Orbiter Science Team and the data they produced provided a large contribution to the success of the Lunar Modeling and Mapping Program. There are other existing activities and expertise that were also leveraged. This is how the USGS became involved with the Lunar Mapping and Modeling Program.

## Slide 3: LMMP Products
Global, Regional and Local Scale Maps
  Visible Imagery Base Maps
  Topographic Maps
    Surface Digital Elevation Models
    Hazard Assessment Maps
    Elevation Contour Maps
  Lighting Maps
  Temperature Maps
  Gravity Models
  Resource Maps
  Other
Integrated Surface Visualization
  Web-based & Desktop Clients
  Format/Interface Standards
  Extensibility
    To other data products and other planetary bodies
Notes: LMMP produced many products and DTMs and Mosaics are a part of that data
Mosaics and DTMs from Apollo panoramic camera ( 3 sites by USGS)
Mosaics and DTMs fro LRO NAC images ( 20 sites by USGS)

## Slide 4: Constellation Regions of Interest
50 sites - selected
  45 sites covered shown in image
  2 polar regional mosaics - NPO and SPO on image
Possible future landing sites or representative terrain of future landing sites
Intended for engineering of Altair Lander, landing and surface operations simulations, actual landing navigation and surface operations

## Slide 5: Source Material
LROC NAC images
  LROC Science Operations Center
  Smithed SPK SPICE kernels - LOLA team cross over
  GSFC reconstructed SPICE data (CKs and SPKs)
Apollo Panoramic
  Johnson Space Center → Arizona State University
    Paris et al. abstract # 2273 – Thursday Poster
  Controlled - ULCN 2005 and readjusted to the LOLA track data.
  Image support data - National Space Science Data Center
LRO LOLA Reduced Data Records – March 2011 release
  Tracks
  Gridded data products
Notes: Emphasize LOLA kernels were very useful

## Slide 6: USGS Products
Site and regional products
23 DTMs covering 21 sites
  Apollo Pan (3) and LROC NAC (20)
  up to 40 x 40 km, 1.5 - 5 m post spacing (resolution)
    0.028% of the Moon, 4.8 billion posts!
23 site mosaics covering 21 sites
  Apollo Pan (3) and LROC NAC (20)
  up to 40 x 40 km, 50-100 cm resolution
Controlled North and South Polar mosaics
  from the pole to 85.5° latitude, 1 m resolution
    Lee et al. abstract # 2507 - Thursday Poster

## Slide 7: USGS Products – Apollo 15 site
Mosaic
Slope Map
DTM
Color Shaded Relief
Shaded Relief
Confidence Map

## Slide 8: Validation process
Comparison to LOLA data
  LRO NAC images triangulated to LOLA track points
    Horizontal better than 20 - 30 m
  LRO NAC DTMs compared to LOLA spot elevations
    The average DTM has 95% of data within
    Lower : -8.2 ± 3.4 m
    Upper : +8.5 ± 3.8 m
  LRO NAC Mosaics
    ISIS 3 jigsaw results compared to SOCET SET triangulation
    Control network checked for complete connections
    Mosaic inspected for offsets between images
    Mosaic compared LOLA DTM shaded relief images

## Slide 9: Validation process - DTMs
Comparison to LOLA spot elevations
Mean | Std. Dev. | Max. | Min | # pts
0.1 m | 4.5 m | -38.3 m | 34.8 m | 63,920
95% range -9.5 to 10.6 m
10 x 10 km is 100% covered
20 x 20 km is 72.1% covered
40 x 40 km is 40.7% covered
10 KM
20 KM
40 KM

## Slide 10: Validation process - DTMs
DTM elevation minus LOLA track elevation data
10 x 10 km is 100% covered
20 x 20 km is 72.1% covered
40 x 40 km is 40.7% covered
10 x 10 km is 100% covered
20 x 20 km is 72.1% covered
40 x 40 km is 40.7% covered
±4.5 m
Standard Deviation
Offset in Tracks
Tracks with large errors

## Slide 11: Validation - Across Teams
Final results to be published
Beyer et al., 2011, 42nd LPSC # 1608
Beyer et al., 2010, 41st LPSC # 1533
  Arizona State University
  USGS
  The Ohio State University
  JPL
  German Aerospace Center
  University of Arizona

## Slide 12: Validation - Apollo 15 Site USGS products only
DTM 1 - M102128467 and M102142784
DTM 2 - M102135625 and M102142784
  Remove shadow areas
  Early mission - images at higher altitude
Majority of differences within expected precision
Mean difference 1.1 m
standard deviation 2.5 m
95% range -3.3 to 6.2 m
Differences are not random
  Structure related to stereo models
  Might be related to unmodeled camera motion
  Might be related to automatic correlation process
N
1
2
3

## Slide 13: Validation - Tsiolkovskiy Crater Site USGS products only
DTM 1 - M143778723 and M143785506
DTM 2 - M167363261 and M167370048
Differences larger than expected precision
Mean difference -0.3 m
standard deviation 4.1 m
95% range –7.8 to 7.1 m
N
Differences are not random
  Structure related to stereo models
  Might be related to unmodeled camera motion
1
2
3

## Slide 14: Summary - Products
Products available on LMMP Portal
  http://lmmp.nasa.gov
Provides high resolution cartographic products
  Mosaics – 0.5 to 1.0 m resolution
  DTMs – 1.5 to 5.0 m resolution
Absolute Horizontal accuracy | better than 20 – 30 m
Absolute Vertical accuracy | better than 10 m